## Slide 1: Enhanced Mobility Anchors

## Slide 2: Enhanced mobility anchoring work item in dmm chapter
Enhanced mobility anchoring: define protocol solutions for a gateway and mobility anchor assignment and mid-session mobility anchor switching that go beyond what has been specified, for example, in RFC 6097, 6463, and 5142. Traffic steering associated with the anchor switch is also in-scope if deemed appropriate.

## Slide 3: Background: LM and FM in RFC7429
Internetwork Location Management (LM) function: managing and keeping track of the internetwork location of an MN. The location information may be a binding of the IP advertised address/prefix, e.g., HoA or HNP, to the IP routing address of the MN or of a node that can forward packets destined to the MN. It is a control plane function.
Forwarding Management (FM) function: packet interception and forwarding to/from the IP address/prefix assigned to the MN, based on the internetwork location information, either to the destination or to some other network element that knows how to forward the packets to their destination.

## Slide 4: Background: Functions involved in anchoring
The following functions seem essential to anchoring:
  Allocation of IP prefix/addr and Route advertisement.
Other functions of anchor in different proposals: each function is not necessarily present in all the solutions:
  (1) packets to/from the MN traverse through.
  (2) indirection, e.g., tunneling
  (3) information, e.g., binding HoA and CoA
  (4) sends route update, e.g., using BGP

## Slide 5: Description on IP address anchoring
An IP address, i.e., Home Address (HoA), or prefix, i.e., Home Network Prefix (HNP) allocated to a mobile node is topologically anchored to a node when the anchor node is able to advertise a connected route into the routing infrastructure for the allocated IP prefixes.

## Slide 6: Category
Address anchored in current net of attachment
Address anchored not in current net of attachment
Changing IP address
keeping IP address
Moving IP address
Indirection of a flow
Changing indirection

## Slide 7: Address anchored (RA and Prefix allocation) in current network of attachment
Net1
Net2
Indirection flow(IP1,…)IPAR2
AR1: RA(IP1)
Indirection Flow(IP1,…)MN
AR2: RA(IP2)
MN: IP2, flow(IP2,…)

## Slide 8: Address anchored (RA and Prefix allocation) not in current network of attachment
Net1
Net2
Indirection flow(IP1,…)IPAR2
AR1: RA(IP1)
Indirection Flow(IP1,…)MN
AR2: RA(IP2)
MN: IP2, flow(IP1,…)

## Slide 9: Changing IP address (address anchored in current network of attachment)
move
Net1
Net3
Net2
Indirection flow(IP1,…)IPAR2
AR1: RA(IP1)
Indirection Flow(IP1,…)MN
AR2: RA(IP2)
MN: IP2, flow(IP2,…)
Indirection flow(IP1,…)IPAR2
AR3: RA(IPCN)
CN: flow(IP2,IPCN, …)
MN: IP1, flow(IP1,…)

## Slide 10: Moving IP address (address anchored in current network of attachment)
move
Net1
Net3
Net2
Indirection LM
AR1: RA(IP1)
Indirection LM
AR2: RA(IP2,IP1)
MN: IP2, flow(IP1,…)
Indirection flow(IP1,…)IPAR2
AR3: RA(IPCN)
CN: flow(IPCN,IP1,…)
move
MN: IP1, flow(IP1,…)
BGP,PD/SDN

## Slide 11: Keeping IP address (address anchored not in current network of attachment)
move
Net1
Net3
Net2
Indirection flow(IP1,…)IPAR2
AR1: RA(IP1)
Indirection Flow(IP1,…)MN
AR2: RA(IP2)
MN: IP1, flow(IP1,…)
MN: IP2, flow(IP1,…)
Indirection flow(IP1,…)IPAR2
AR3: RA(IPCN)
CN: flow(IP1,IPCN, …)

## Slide 12: Indirection of a flow (keeping IP address)
move
Net1
Net3
Net2
FM: flow(IP1,…)AR2 LM: IP1IPAR2
AR1: RA(IP1)
flow(IP1,…)MN
AR2: RA(IP2)
MN: IP2, flow(IP1,…)
Indirection flow(IP1,…)IPAR2
AR3: RA(IPCN)
CN: flow(IPCN,IP1,…)
MN: IP1, flow(IP1,…)

## Slide 13: Changing indirection (keeping IP address)
move
copy
Net1
Net3
Net2
FM: flow(IP1,…)AR2 LM: IP1IPAR2
AR1: RA(IP1)
flow(IP1,…)MN
AR2: RA(IP2)
MN: IP2, flow(IP1,…)
FM: flow(IP1,…)AR2 LM: IP1IPAR2
AR3: RA(IPCN)
CN: flow(IPCN,IP1,…)
MN: IP1, flow(IP1,…)

## Slide 14: Comments and suggestions are welcome
Thank you